## Slide 1: You Must Learn This!!
More on Interrupts and Context Switching Buddy!!

## Slide 2: Context and periods for context switching
Getting an address from where the new function begins, loading that address into PC and then executing the called function’s instruction will change a running function at CPU to another. (new function will be executed, by keeping a page mark for the function from where the new function is called)
Before executing new instructions of the new function the processor or OS also saves the current program’s status word, registers and program contexts.
If not done by OS or Processor, then the new functions, instruction should do that.
This is because these (program’s status word, registers ) information might be needed by newly called function.
Current Program Context
PC (Program Counter)
SP (Stack Pointer)
CPU registers
Processor Status Register
Current Program Context

## Slide 3: Context and periods for context switching
The context must save if a function program or routine left earlier has to run again from the state which was left.
When there is a call to a function (i.e. routine in assembly language) the function or ISR or exception handling function executes 3 main steps:
  Saving all CPU registers including processor status word, registers and function’s current address for next instruction in PC. Saving address of the PC on to the stack is required if there is no link register to point to the PC of left instruction of the earlier function. Saving facilitates the return from new function to the previous function.
  Load new context to switch to a new function.
  Execute the new function.
  These three steps are together called as context switching.
Save current function or ISR context on a stack and load new function
Context Switching

## Slide 4: Context and periods for context switching
The last action of any routine or function is always a return.
The following steps occur during the return from the called function:
  Before return retrieve the previously stored status word, registers and other context parameters.
  Retrieve address from stack or link register and adjust the contents of the stack if needed.
  Execute the remaining part of the old function from where the new function is called.
  Let’s check it out diagrammatically!!!
Steps on switching for new routine
1. Save current routine context on stack and load new routine context.
2. Execute the new routine codes
3. On return save the new routine context and switch for the previous routine by retrieving the saved context
Context Switching
Context Switching
Current routine

## Slide 5: What is an interrupt
Every embedded system typically takes input from its user or environment. The interrupt mechanism is one of the common ways to interact with the user.
Consider a situation in which microprocessor has to process inputs from three peripheral devices.
µP
D2
D3
D1
A microprocessor is interacting with 3 devices!

## Slide 6: What is an interrupt ???
One way to accomplish this is thro polling! (i.e. asking each device for input)
The algorithm for this could be
  This keeps the microprocessor always busy. It is either polling for the input or it will be processing the input. This method has more CONS than PROS with one definite drawback of making the microprocessor to work forever.
  The other mechanism is interrupting. In this mechanism the device informs, i.e., interrupts the microprocessor whenever it has some input for the microprocessor.
  The clear advantage of this method over the polling method that the processor is free to do other work. (Running other applications   )
While the program is running {
Poll Device D1 for input
If the input is present, process input from D1
Poll Device D2 for input
If the input is present, process input from D2
Poll Device D3 for input
If the input is present, process input from D3
}
Algorithm for three polled devices

## Slide 7: Interrupt – Types
INTERRUPTS
HARDWARE
SOFTWARE
Normal Interrupt
Exception
1. If the Microprocessor is interrupted by external device / hardware., then we can classify it as hardware interrupt
1. Interrupts can be raised also by executing software instructions. It is called software interrupts.
1. If the interrupt is planned then it is called Normal Interrupt
1. If an interrupt is unplanned then it is classified as Exceptions.
Periodic Interrupts: if the interrupts occur at fixed intervals of timeline, then they are called periodic
Aperiodic Interrupts: if the interrupts occur at Any point of time it is aperiodic. (Anticipating a key press from user)

## Slide 8: Interrupt latency
One obvious question that everyone will get in mind is
“ How fast my embedded system will respond to each interrupt??”
The answer for this question depends on numerous factors:
  The period of time it takes to execute any interrupt routines for interrupt that are of higher priority than one in question!! 
  How long it takes for the microprocessor to stop what it is doing, do necessary book keeping, and start executing instructions within the interrupt routine!
  How long it takes to store the context ???
The interval between the occurrence of an interrupt and start of execution of the ISR is called interrupt latency.

## Slide 9: Interrupt latency – Factors that govern interrupt latency
Make your interrupt routines short!
  Processing time used by an interrupt routine slows response for every other interrupt of the same or lower priority.
  Although lower priority interrupts are most probably lower priority because their response time requirements are less critical.
  This is not necessarily license to make their response dreadful by writing a time consuming interrupt routine for higher priority interrupt.
  An Example which would be better depiction for this case! Lets talk about it now!!!

## Slide 10: Interrupt latency – Example - Make your interrupt routines short!
Suppose that you are writing a system that controls a factory and that every second your system gets many interrupts (almost say a dozen) to which it must respond promptly to keep the factory running smoothly.
If that your system monitors a detector that checks for gas leaks, and your system must call fire department and shut down the affected part of the factory if gas leakage is detected.
Now it is very likely that the interrupt routine that handles the gas leakage needs to be relatively high priority, since it would be bad idea for other interrupts to get micro processors attention.
However the system needs to continue operating the unaffected part of the factory, so the gas leak interrupt routine must not take up too much time. If calling the fire department – a process that will take several seconds, at least included in the gas leak interrupt routine, then dozens of other interrupts will pile up while this is going on, an rest of the factory may not run properly. Therefore the telephone call should not be a part of interrupt routine.

## Slide 11: Interrupt latency
When an interrupt occurs the service of the interrupt by executing ISR may not start immediately by context switching.
The interval between the occurrence of an interrupt and start of execution of the ISR is called interrupt latency.
CASE:1
  The time taken for context switch is being referred as Tswitch
  When the interrupt service starts immediately on context switching , the interrupt latency is equal to the context switching period.
  When instructions in a processor take variable clock cycles, maximum clock cycles for an instruction are taken into account for calculating the latency.
Interrupt latency = t’ only where t’ is the context switching time for saving the running program context and loading the new routine context

## Slide 12: Interrupt latency
CASE:2
When interrupt service does not start immediately but context switching starts after all the ISRs corresponding to the higher priority interrupts complete the execution.
if the sum of time intervals for completing higher priority ISRs equals ∑Texec, then the interrupt latency equals Tswitch + ∑Texec .
Processor
ISR
High Priority ISR
Assume that this is a Current ISR of higher priority
After Present ISR of Higher priority interrupt completes execution, this ISR will be given the processor time.

## Slide 13: Interrupt latency
CASE:3
We disable the interrupt system when a routine enters a critical section and enable the interrupts when routine exits the critical section.
A routine of function or ISR may consists of codes for critical region instructions and before the critical section codes all the interrupts are disabled and enabled by the end of critical section.
Lets say Tdisable is the period for which a routine is disabled in its critical section.
The interrupt service latency from the routine with the interrupt disabling instruction will be Tswitch + ∑Texec + Tdisable .
I S R
I S R
Critical Section Codes
Interrupt latency = Tswitch + ∑Texec + Tdisable . Where Tswitch is context switching time. Tdisable is time for which the interrupts remain disabled. ∑Texec is the time for which other high priority routines are executed