## Slide 1: DMA
AN EXPLORATION

## Slide 2
DMA( Direct memory Access):
This is a bus operation that allows Reads and Writes are not controlled by the CPU.
A DMA transfer is controlled by the DMA controller , which requests control of the Bus from the CPU.
After gaining control DMA performs Read and Write operations directly between devices and memory.
The DMA requests the CPU to provide 2 additional signals :
1. BUS Request : I/p to the CPU thro’ which DMA asks for the ownership of the BUS.
2. Bus grant: signals that the bus has been granted to the DMA controller.

## Slide 3
CPU
DMA controller
Device 2
Clock
R/W’
Address
Data
Memory
Data ready’
Bus request
Bus grant
DMA( Direct memory Access):

## Slide 4
Alternate way:
CPU
DMAC
Device
Memory
bus request
bus grant
DMA( Direct memory Access):

## Slide 5
A device that can initiate its own bus transfer is called the Bus Master.
DMA controller uses Bus request and Bus Grant to gain control of the Bus using classic four cycle hand shake.
The bus grant is asserted by the DMA controller when it wants to control the bus and grant is asserted by the CPU when the bus is ready.
The CPU will finish all the pending transactions b4 granting control to the DMA controller. When it does grant control it stops driving the other bus signals; like R/w’, address etc.,
DMA( Direct memory Access):

## Slide 6
Once the DMA controller gained control it can perform Read and write operation.
Memory does not know whether the operation is performed by CPU or DMA.
After the transaction is complete the DMA returns the bus to CPU by de asserting the bus request, causing the CPU to De assert the bus grant.
CPU controls the DMA controller through the registers in DMA controller. Three registers are available.
DMA( Direct memory Access):

## Slide 7
Starting Address Register:
It specifies where the transfer has to begin.
Length register:
it specifies the number of words to be transformed.
A status register:
it allows DMA to be operated by the CPU.
DMA( Direct memory Access):

## Slide 8
The CPU initiates the DMA by setting the starting address and length registers approximately and then writing the status register to set its starting transfer bit.
After operation is complete DMA controller interrupts the CPU to tell that the operation is completed.
CPU cannot use the bus during DMA operation.
if it has enough instructions and data in cache and registers, it may do some useful work and may not notice the DMA operation. But once the CPU needs the bus it stalls until the bus mastership is back.
DMA( Direct memory Access):

## Slide 9: DMA
To prevent the CPU from being idle for too long, most DMA controllers implement modes that occupy the bus for only a few cycles at a time.
For example the transfer may be made as 4,8 or 16 words at a time.
After each block, DMA controller returns control of the bus to CPU and goes to sleep for a preset period, after which it requests the bus again for next block transfer.